Round5 – Hardware overview
By Michal Andrzejczak

---
Round5 – CPA_PKE_ENC
1. 1. Unpack PK
2. 2. Create matrix A (from seed) - cSHAKE
3. 3. Create matrix R (from another seed) - cSHAKE
4. 4. Polynomial Multiplication (12 bit x {-1,0,1})
5. 5. Rounding (from 12 bit to 8 bit)
6. 6. Polynomial Multiplication (8 bit x {-1,0,1})
7. 7. Rounding (from 8 bit to 4 bit)
8. 8. Add msg
9. 9. Pack CT

---
Round5 - CPA_PKE_DEC
1. 1. Create matrix S (from sk) - cSHAKE
2. 2. Unpack ct
3. 3. Decompress matrix
4. 4. Polynomial multiplication (8 bit x {-1,0,1})
5. 5. Diff results (from point 3 sub point 4)
6. 6. Rounding(from 8 bit to 1 bit)

---
Polynomial multiplication
1. 1. Lift poly
  1. a) input: polynomial mod 2048
  2. b) input: polynomial mod 256
2. 2. NTRU polynomial multiplication
  1. a) multiplication by trinomial mod 2048
  2. b) multiplication by trinomial mod 256
3. 3. Unlift poly
  1. a) input: polynomial mod 2048
  2. b) input: polynomial mod 256
  3. c) long data dependency path! c[i] = c[i-1]-a[i]

---
Main difficulties:
1. 1. Round Poly:
    1. a) three different parameter set (2 for encyption, 1 for decryption)
    2. b) can be implemented as three separated units
    3. c) or one unit performing similar operations
    4. d) executes in 1 clock cycle (maybe use less elements with shift register)
2. 2. Polynomial Multiplication
    1. a) operates modulo two different values
    2. b) can calculate both values at once, only output should be duplicated (first port for result mod a, second for result mod b)
3. 3. Lift & Unlift Poly
    1. a) operates on two parameter set, similar case as with polynomial multiplication

---
Round5- Building blocks
2. 1. CPA_PKE: sampling(cSHAKE), poly mult
3. 2: CPA_KEM: CPA_PKE + 2 x SHAKE hash function
4. 3. CCA_KEM: CPA_PKE + 3 x SHAKE hash function
  4. CCA_PKE: CCA_KEM + round5_dem function